## Slide 1
Practical 7: Non-steady heat equation
Glaciology EESCGU4220
Aims:
Learn about boundary conditions
Learn more about “parameter space” and how to search it.
Understand what controls temperature in cold-based ice sheets.

## Slide 2: Boundary conditions
Surface energy balance (Lecture 4)
Basal energy balance
--- geothermal heat flux, friction: , hydrology
  Cold-based ice:
  Geothermal heat flux is set at the base.
  Neumann boundary condition (one that fixes the derivative of T)
z
T
0
  Warm-based ice:
  Tb = melting point
  Dirichlet boundary condition (one that fixes the value of T)
z
T
0

## Slide 3
1. Solve the heat equation:
basal boundary condition:
where G is geothermal heat flux, 0.060 W/m2 and k is thermal conductivity in the ice, 2.3 W/mK
Steady-state T
2. Plot steady-state basal T against ice thickness
3. Plot steady-state basal T against accumulation rate
4. Plot steady-state basal T against ice thickness AND accumulation rate on the same plot (2-D parameter space)
Time-varying T (phase space) 5. Phase space plot (surface T vs. basal T) and how that varies with
w
0
Accumulation rate
a
z